## Slide 1: Track Short Course: TrackRT Installation
Thomas Herring, MIT
Room 54-820A
tah@mit.edu

## Slide 2: TrackRT Introduction
TrackRT is the real-time version of track that uses BNC
trackRT requires the BKG NTRIP Client (BNC) and QT libraries and include files. Ntrip is the Networked Transport of RTCM via Internet Protocol and the client program BNC provides access to the real-time data streams and casts the data via an internet port. GNSS raw data in a structure that is decoded by trackRT.
Currently trackRT only uses the GPS data streams. TheNTRIP system is discussed at http://igs.bkg.bund.de/ntrip/. The BNC program can be downloaded from http://igs.bkg.bund.de/ntrip/download. The BNC documentation contains the instructions for obtaining the QT libraries and include files needed for its installation from source files. trackRT only needs the executable version of BNC. The QT software can be obtained directly from Nokia at the site http://qt.nokia.com/downloads
The trackRT help file contains more instructions

## Slide 3: TrackRT operation
Once trackRT is installed, the basic operation is to start copies of BNC that will cast the data from specific sites of interest.
Once BNC configuration has been established and saved to a file; BNC can be started to run with no window (-nw option) and a configure file for each network of site e.g., bnc –nw –conf Net01Config.ini
TrackRT can then process any or all of the sites being cast. So far we have always, paired the BNC and trackRT runs (i.e., once one copy of trackRT is connected to a port, no other copy can access that port.
trackRT and BNC do not need to be on the same host provided the port is open.

## Slide 4: Installing trackRT
The Makefile for trackRT needs to be modified to point to the correct locations of the Qt libraries and maybe change some of the flags on the compile lines.
Using qmake in the BNC source file directories to generate the Makefile for BNC
Linux installs seem OK but MacOSX still has some problems. (On my system this seems to be due to multiple versions of g++ and gfortran which have incompatible options such as –arch).

## Slide 5: Installing trackRT
The Makefile needs to be modified to point to the QtNetwork, QtCore libraries and include files
The paths to these are set with options like
QTLIB = /opt/local/lib
QTINC = /opt/local/include/
In the Makefile
TrackRT main is a c++ program which is linked with gfortran subroutines.

## Slide 6: Other operational aspects
Since trackRT runs continuously, it needs up to data satellite ephemeris data and so a cron is normally run that downloads the latest IGS SP3 orbit files. The help for trackRT contains an example cron script.
In setting the crontab entries you should run it at the correct UTC times. These times will depend on the configuration of your system time.

## Slide 7: TrackRT runstring
Runstring:
% trackRT <options>
where options are
-m <machine> Host name of system with real-time data port (Normally BNC would be running on this system)
(Default local host)
-p <port> Port number on host supplying the data stream (Manadatory input).
-f <command file> trackRT command file (similar to track command file)
-r <ref code> 4-char code for reference site.
-d <list of 4-character codes> list of sites to be processed.

## Slide 8: TrackRT runstring
If list of sites is not specified all sites in data stream will be processed (there is a limit on maximum number of sites that can be processed depending on max_site in trackRT. The reference code should NOT be given here.)
-n <root name> Specifies a root name to which output will be directed (.out is appended for stdout output). Use ? in the pos_root, sum_file and csv_file names the ? will be replaced by this string.
Command file name must be given.

## Slide 9: TrackRTr runstring
% trackRTr <options>
Same list of option although -m, -p have no effect
-d <list of rinex files> list of rinex files (site names are generated from the first 4-characters of rinex file names)
-r <4-char code reference site>

## Slide 10: Start BNC/TrackRT
Before starting the lecture on trackRT commands, we will start BNC and trackRT now running on an MIT host.
The sites to be processed will be some PBO stations.
Track command trackRT -p 3765 -f trackRT_pbo.cmd -r P498 \ -d P505 P509 P494 P496 -n PBO
http://chandler.mit.edu/kmeduna/ can be used to view results