## Slide 1: Track Short Course: TrackRT commands
Thomas Herring, MIT
Room 54-820A
tah@mit.edu

## Slide 2: TrackRT/TrackRTr commands
TrackRT and TrackRTr share many commands in common with track but there are some additional commands and some classes of commands that operate differently due to the real-time nature of the processing.

## Slide 3: Minimum commands in command file
SP3_DIR : (unless sp3 files are in the current directory)
SITE_POS: Site positions must be given for every site to be processed. (Real time streams do not contain positions (unlike rinex headers in track).
SITE_STATS: To set the apriori sigma and process noise for the sites. NOTE: The reference site position should be set to zero for the apriori sigma and process noise. Typical site_stats would be with cit1 as the reference site. (If reference not set to zero, all site positions estimated).
site_stats
all 0.1 0.1 0.1 0.025 0.025 0.025
cit1 0.0 0.0 0.0 0.0 0.0 0.0
ATM_STATS: By default atmospheric delays are not estimated, and normally
these should be. Normally the reference site is set to zero
when site separations are less the 500-1000km. Typical atm_stats
command would be
atm_stats
all 0.20 0.00010 0.000 ! Unit m/sqrt(sec) -> 0.0001 = 0.03 m/sqrt(day)
cit1 0.00 0.00000 0.000

## Slide 4: Also often needed commands
If mixed antenna and receiver types are used
ANTE_OFF: To specify the antenna heights and types and receiver types
ANTMOD_FILE: Must be given to get the antenna phase center models
RCV_TYPE: Needed for mixed receiver types (entry can be specified in ANTE_OFF also and this command would not be needed).
DCB_FILE: Up to date, data code bias (DCB) file (part of GAMIT ftp area).
Including
UPDATE_FILE is useful so that trackRT can be controlled on the fly.

## Slide 5: Input/output commands
@ SP3_DIR <Directory> <center>
<Directory> -- Directory where sp3 files are stored
<center> -- Center for orbits (default igs, igr and igu also tested)

## Slide 6: IO commands
@ POS_ROOT <root> <duration>
Set the root part of the name for the outout files.
<root> Root part of name. When ? included in the <root>, the ? is
replaced with the -n string.
<duration> Duration of data in each file. The designations of d, h, or m
may be used to specify the units of days, hours, minutes.
Default is d.
The position file names take the form: (see commands below)
<root>.<outtype>.<site>.<start time>.<datatype>
The resolution of the <start time> which is modulo the output interval
depends on the output duration. For output durations greater than or
equal to 1-day, the time is given as YYYYMMDD. For intervals shorter
than 1-day, it is YYYYMMDD:HHMN. Minimum output interval is 1 minute.

## Slide 7: IO commands
@ SUM_FILE <root>
Sets the root part of the summary file name. Using ? in the name with be replaced by the -n string. (Default if command is not given is trackRT or the -n string when -n used). File names are time tagged according to the pos_root output interval.

## Slide 8: IO commands
@ CSV_ROOT <root>
Set the root part of the name for comma separated values (CSV) output file. These files are used for AmCharts web plots.
@ DCB_FILE <file name>
Set the name of the data-code-bias (DCB) file. This file is part of the GAMIT tables directory and should be updated regularly. It is used to remove biases in the Melbourne-Wubbena widelanes. The receiver type can be specified with the RCV_TYPE or ANTE_OFF commands.

## Slide 9: IO commands
@ ANTMOD_FILE <file name>
Sets the name of a standard IGS antex file with phase center models for the GPS ground antennas. Antenna types at specific sites are given with the ANTE_OFF command. This command my be used multiple times for site specific model with new models replacing previously read ones.
@ UPDATE_FILE <file name>
Allows new trackRT commands to be issued during a run. Once the file is
read it needs to be deleted before the trackRT will re-read it. File is
only read if it exists. NOTE: File should be removed before trackRT is
run or else it will be read when the command file is read (ie., it will
overwrite the commands in the command file.

## Slide 10: IO commands
@ OUT_TYPE <NEU+GEOD+XYZ+DHU>
Specifies types of output coordinates. All types can specified in a single string with no spaces. The types are
NEU -- North, East, Up differences from the reference site or from the coordinates given in the REF_NEU command.
GEOD -- Geodetic latitude, longitude and height (in the GEOD format, the total atmosheric delay is given, while in the other formats the adjustment to the apriori delay is given).
XYZ -- Cartersian XYZ coordinates
DHU -- Delta horizontal and Up coordinates from the apriori coordinates of each site (default output type)
@ OUT_SIG_LIMIT <sigma (m)>
Sets the maximum sigma of a position estimate for it to be output. If pseudorange data types are used, the default value of 1 m needs to increased to 10-100 meters.

## Slide 11: Analysis commands
@ DATA_NOISE <L1 (m)> <L2 (m)> <P1 (m)> <P2 (m)> <Elev Weight> [PRN]
Same as track
@ DATA_TYPE <type>
Same as track (L1 only should be possible but not checked).
@ USE_GPTGMF
Same as track (recommended for all runs)
@ SITE_POS
@ Site <X (m)> <Y (m)> <Z (m)> <Vx (m)> <Vy (m)> <Vz (m)> <Epoch (yrs)>
Same as track

## Slide 12: Analysis commands
@ ANTE_OFF
@ Site <ARP dN (m)> <ARP dE (m)> <ARP dU (m)> <Antenna Name> <Receiver Code>
Specifies the type of antenna and its position of antenna reference point (ARP) at each site. The antenna name including radome should be specified with the official IGS name for a standard ANTEX file or with a unique name that appears in the ANTEX file for site specific calibrations. (Note: There is one additional character in the station.info long antenna and this extra character before the radome name must be removed. The antenna name and radome can be copied directly from the rinex file if present. One more ANTEX files must be specified with the ANTMOD_FILE command for the antenna names to be useful. The receiver type DCB code can be optionally specified here as well (See RCV_TYPE command).

## Slide 13: Analysis commands
@ RCV_TYPE
@ Site <Receiver code N/P/C>
Specifies the type of data-code-bias (DCB) correction needed for the receiver. Code specifies the type of L1 and L2 ranges being measures. The choices are
P -- Pcode, C -- C/A and N C/A with cross correlation for L2 range. The codes can be found in gamit/tables/rcvant.dat. These codes can also be given in the ante_off command. An up-to-date DCB_FILE command must be used to specify the DCB biases. The files are available from the MIT ftp site and update once per month.

## Slide 14: Analysis commands
@ SITE_STATS
@ Site <Apriori Sigmas in XYZ (m)> <RW noises in XYZ (m/sqrt(sec))>
Same as track except units here are per sqrt(seconds) always (not time_unit command here).
@ ATM_STATS
@ Site <Apriori Zenith delay sigma> <RW noise in Zenith delay> <RW dH/dt noise>
Same as track with second as time unit.

## Slide 15: Ambiguity Resolution
trackRT uses a combination of the Melbourne-Wubbena widelane (MW-WL), the extra widelane (EX-WL) and the floating point estimates of the ionospheric free ambiguity (LC) to resolve integer ambiguities.
If we denote the number of integer cycle ambiguities at L1 and L2 by N1 and N2,
  MW-WL is an estimate of N1-N2 based on phase and range data;
  EX-WL = N1 - f1/f2 N2 and is an integer for L1 cycles, but 1.283 N2 for L2 cycles;
  LC = 2.546 N1 - 1.984 N2.
The EX-WL is unaffected by geometric ranges changes, but does depend on the ionospheric delay.
For short baselines, the EX-WL should be near zero for correct choices of N1 and N2.
The LC residual should also be near zero when N1 and N2 are correct.

## Slide 16: Ambiguity Resolution
The problem in ambiguity resolution is that different choices of N1 and N2 can make different linear combinations small.
For example, errors in N1 and N2 of 3 and 4 cycles will change LC by 0.298 cycles (56.6 mm), MW-WL by 1 cycle and EX-WL by 2.132 cycles (405 mm).
On long baselines, at low elevation angles, ionospheric delays of 400 mm (2 cycles) are common.
The most common error is a N1=N2=1 cycle error. For this combination, the MW-WL is unaffected and LC changes by 0.562 cyc (107 mm) and EX-WL by 0.283 cyc (54 mm). Even on relative short baselines, 54 mm ionospheric delays are common

## Slide 17: Commands to control ambiguity resolution
@ AMB_SET <RelRank> <FloatSigma (2)> <MWWL Fact> <EXWL Fact> <Min AmbSig> <MaxChi>
Sets parameters for ambiguity resolution. The input parameters are:
<RelRank>
<WL min> Minumum of values need to allow bias fixing
<WL avN> Maximum number to be used in computing sigma of mean MW-WL
<FloatSigma (2)> Minimum sigma for LC and MW-WL for ambiguity fixing
<MWWL Fact> Weighting factor for MW-WL in chi**2
<EXWL Fact> Weighting factor for extra-wide lange
<Min AmbSig> Minimum sigma to assigned to float estimates of ambiguities.
<MaxChi> Max chi**2 value allowed for ambiguity to be resolved.
This command is similar to the float_type command in track

## Slide 18: Commands to control ambiguity resolution
@ EXWL_SET <Jump> <Min Sigma> <Scale> <Elev Fact>
<Jump> -- magnitude of jump in EX-WL to have cycle slip added (default 0.10)
<Min Sigma> -- minimum sigma for mean ex-wl (cycles, default 0.02 cycles)
<Scale> -- Scaling factor for length. Scale 0.1 results in 0.1 cycles over 100 km (default)
<Elev Factor> -- Elevation angle factor that increases sigma as (1 + factor/sin(elev))
This command is set tolerances for adding a new cycle slip to the processing. The length dependent term of different length baselines in the processing.

## Slide 19: Commands to control ambiguity resolution
@ MWWL_SET <Jump> <Min Sigma> <Max Averaging number> <Min number>
<Jump> -- magnitude of jump in MW-WL to have cycle slip added (default 5.0)
<Min Sigma> -- minimum sigma for mean MW-WL (cycles, default 0.10 cycles)
<Max Averaging number> -- Maximum number of values to use to compute mean sigma
<Min number> -- Minimum number needed to resolve ambiguity
Cycle slip detection based on the MW-WL lines

## Slide 20: Commands to control ambiguity resolution
@ DD_SET <Jump (cycle)> <Min Number>
Sets parameters for double difference processing.
<Jump (cycle)> -- Magnitude of jump in double differences on bias fixed data that will introduce a cycle slip
<Min Number> -- Minimum number of double differences for an epoch to be processed. (If too few double differences than errors in the data can not be detected and this can cause large position errors, default of 4 double differences allows redundancy).

## Slide 21: Commands to control ambiguity resolution
@ RMS_EDIT_TOL <n-sigma Tolerance> <min sigma> <Reset number>
<n-sigma tolerance> is an n-sigma condition where sigma is based on data noise model.
<min sigma> Minimum phase sigma to use so that no phase residual less than <min sigma>*<n-sigma tolerance> are deleted
<Reset number> number of sequential delete data, before ambiguity and cycle slips are reset (assumed missed cycle slip).
This a post-fit editing option to remove bad data. Data epoch is re-processed if data are deleted.

## Slide 22: Testing and Evaluation
@ STATUS <type> <# epoch>
Writes status information to the current summary file at <# epoch> intervals
The types of reports are given by "type"
P -- Parameter estimates
A -- Ambiguity resolution report (shows resolved and unresolved)
W -- Widelanes (Melbourne-Wubbena and Extra-widelanes)
R -- Postfit residuals are current epoch
C -- Report current A and W entries only
type PAWR will output all reports.

## Slide 23: Testing and Evalutions
@ NUM_EPOCHS <number>
<number> is the number of epochs of data to be processed before stopping. When short duration files are output (POS_ROOT command) the number of epochs may not be reached because the epoch counter is reset with each new file.
@ START_TIME <yy mm dd hh min sec.>
Used to set the start time. Useful with trackRTr to have the processing start at the same time as the realtime stream.

## Slide 24: Testing and Evaluation
@ DEBUG <Up to 10 epoch numbers in pairs>
Sets which epochs will report detailed debug and status information (see STATUS command
as well). The pairs are used as:
1,2 -- Mostly model information. Useful if data are generating large residuals
3,4 -- Parameter estimates, widelanes, residuals
5,6 -- One-way OMC and single differences
7,8 -- Not Used
9,10 -- When 9 is non-zero, antenna model and SP3 information is output.
This command is often used in the update_file command file.

## Slide 25: Testing and Evaluation
@ RESET <ALL/list of sites>
Reset command. Resets the filter state vector and resolved ambiguities for a list of sites or ALL sites (generally used in the update_file to fix problems)
@ EXCLUDE_SVS <list of PRN numbers to be excluded>
Excludes satellites from being processed. Useful when a satellite is not in an SP3 file or not available during the times there are data.
Example: exclude_svs 26 22 13

## Slide 26: Testing and Evalution
@ UPDATE_FILE <file name>
Allows new trackRT commands to be issued during a run. Once the file is read it needs to be deleted before the trackRT will re-read it. File is only read if it exists.
NOTE: File should be removed before trackRT is run or else it will be read when the command file is read (ie., it will overwrite the commands in the command file.
Generally, we keep a file of a different name and then copy it to the <file name> here when we want it to be used.

## Slide 27: Lines written to summary file
Cycle slip detection: CSLIP Ep 540 Site THMG G 29 DMW-WL/Tol 4.31 4.00 DEX-WL/Tol 1.78 0.20 cyc, Elev 10.00 deg
This case show a slip detected with MW-WL and EX-WL jumps. The values of the jump and the current tolerance are reported.
Double difference residual slip
CSLIP Ep 12 Site P496 G 15 DD RESID -4.80 Tol 0.50 cyc, Elev 23.45 deg

## Slide 28: Lines written to summary file
Resolve ambiguities: When ambiguities are resolved, three lines are output giving the statistics (lines are wrapped here)
AMBFIX WMAP PRN29 EP 599 RelRank 101.76 FC ------ dL12 4 3 Dchi 6.54 691.02 AMB 36
AMBWLS WMAP PRN29 EP 599 RG 133 599 FX 3 iL12 0 0 Means -0.16 -0.05 RMS 0.74 0.06 # 467 eN12 -0.54 -0.38 AzEl 274.32 12.35
AMBCON WMAP PRN29 EP 599 NCont 3 MW Res -0.159 0.185 Chi2 0.74 EX Res -0.051 0.068 Chi2 0.55 LC Res -0.046 0.020 Chi2 5.25
Help file explains entries: RG is range of data used.

## Slide 29: Other outputs
Other outputs from the STATUS command are explained in the help file
Lines are too long to effectively show here but in the tutorial session we can look at the results.
We now look at some results generated during the talk and from earlier trackRT runs