## Slide 1: Track Short Course: Track Examples
Thomas Herring, MIT
Room 54-820A
tah@mit.edu

## Slide 2: Example cases
Example data sets. For each .gz file, create a folder where the tar files will be untarred (i.e., there is no folder information in that tar files
Examples are:
  MIT_short.tar.gz : Short baseline case
  BAJA_eq.tar.gz : Earthquake surface wave example
  TIGA_bouy.tar.gz : Tidal ocean buoy data set
  Brazil_aircraft.tar.gz : Aircraft flight example with some data problems,

## Slide 3: MIT Short
This is a short baseline data set where we can process in LC mode and compare to an L1+L2 solution.
Same antenna and receiver used at both sites so the antenna and receiver models don’t need to be specified.
Start a new command from scratch.

## Slide 4: BAJA data
This is part of the 5-Hz data set from Unavco for the April 4, 2010 El-Mayor Cucapah earthquake in Baja California
Start here with short baselines (P066 as reference) and then use long baseline (P725 as reference).
Also initially use interval 1.0 for 1-Hz solution.
(3-hrs of rinex are concatenated here; track can handle internal rinex headers).

## Slide 5: Buoy Data set
This is an ocean buoy data that is typically of large movement but almost static data sets.

## Slide 6: Brazil Air
This an aircraft flight for gravity measurements. The baseline is long (~250km) and there are missed cycle slips in the data in a standard track solution (need usr_addbf to put them in).
Some receivers try to fix cycle slips using the same methods track uses to detect them and this can cause problems. (Number of L1 and L2 cycles is small in these cases).
Apriori coordinates also an issue here