## Slide 1
GMTSAR Short Course
UNAVCO, July 2014
David Sandwell, Rob Mellors,
Xiaopeng Tong, Scott Baker
Objectives:
  run GMT and GMTSAR on your own computer
  perform 2-pass InSAR processing on your own computer
  data (ERS, Envisat, ALOS-1) from UNAVCO and ASF
  prepare large stacks of interferograms
  time series (see next UNAVCO InSAR short course August 4 - 6)
Notes: 1

## Slide 2
GMTSAR Short Course
OUTLINE
setup UNIX, GMT, and GMTSAR – test cases
overview of SAR and InSAR – Burgmann et al., 2002
learn to select SAR scenes at UNAVCO and ASF
SAR and InSAR theory
GMTSAR overview, modules, standard InSAR processing
2-D phase unwrapping
batch processing
imaging earthquakes
student presentations
Notes: 2

## Slide 3
passive and active remote sensing – optical and microwave

## Slide 4: Radar
RADAR: “Radio Detection and Ranging”
EM waves - Active System (own illumination)
Principle (like any EM ranging method):
  Create a pulse of oscillating EM energy
  frequency f, and duration 
  scatter
  return of some energy to radar
   = c/f
  R = ct/2, Measures time of flight of EM pulses
[Burgmann et al., 2000]

## Slide 5: Radar Location
RADAR: “Radio Detection and Ranging”
H. Zebker
[Burgmann et al., 2000]

## Slide 6: Radar Geometry
from http://southport.jpl.nasa.gov/desc/imagingradarv3.html
Range
Directions
Track
[Burgmann et al., 2000]
Notes: The length of the radar antenna determines the resolution in the azimuth (along-track) direction of the image: the longer the antenna, the finer the resolution in this dimension. Synthetic Aperture Radar (SAR) refers to a technique used to synthesize a very long antenna by combining signals (echoes) received by the radar as it moves along its flight track. Aperture means the opening used to collect the reflected energy that is used to form an image. In the case of a camera, this would be the shutter opening; for radar it is the antenna. A synthetic aperture is constructed by moving a real aperture or antenna through a series of positions along the flight track.
As the radar moves, a pulse is transmitted at each position; the return echoes pass through the receiver and are recorded in an 'echo store.' Because the radar is moving relative to the ground, the returned echoes are Doppler-shifted (negatively as the radar approaches a target; positively as it moves away). Comparing the Doppler-shifted frequencies to a reference frequency allows many returned signals to be "focused" on a single point, effectively increasing the length of the antenna that is imaging that particular point. This focusing operation, commonly known as SAR processing, is now done digitally on fast computer systems. The trick in SAR processing is to correctly match the variation in Doppler frequency for each point in the image: this requires very precise knowledge of the relative motion between the platform and the imaged objects (which is the cause of the Doppler variation in the first place).
Synthetic aperture radar is now a mature technique used to generate radar images in which fine detail can be resolved. SARs provide unique capabilities as an imaging tool. Because they provide their own illumination (the radar pulses), they can image at any time of day or night, regardless of sun illumination. And because the radar wavelengths are much longer than those of visible or infrared light, SARs can also "see" through cloudy and dusty conditions that visible and infrared instruments cannot.
from http://southport.jpl.nasa.gov/desc/imagingradarv3.html

## Slide 8: amplitude and phase

## Slide 9: coherence and pixel matching

## Slide 10
Pinon Flat

## Slide 11
ERS
Tracks (501 orbits per repeat cycle)
Frames (6041 seconds per orbit)
T356
F2925

## Slide 12: ERS amplitude image

## Slide 13
geometry
foreshortening
layover
shadowing

## Slide 14: zoom of amplitude image

## Slide 15
Magellen SAR
1990-1994

## Slide 16
Magellen SAR 1990-1994 at Venus

## Slide 17
Radar Image Properties
SLOPE
ROUGHNESS
REFLECTIVITY
Surface
Notes: 17
•Left-looking. Left panel, lava channels on the southern slopes of Ovda Regio show the effects of topographic slope. Slopes facing away from the spacecraft (to the east) are elongated and appear to be in shadow, while west-facing slopes are foreshortened and radar-bright.
• The center panel shows Aurelia Crater. The brightness of the crater's ejecta and floor deposits indicates a surface that is very rough at the centimeter-scale-operating wavelengths of the SAR.
• In the right panel, notice that while the landforms do not appear to change much across the image, the western half of the image appears brighter. The western portion of the image is the southeastern portion of Maxwell Montes: At elevations greater than about 4 kilometers above mean planetary radius, the mountains are inherently more reflective, much like aluminum foil is more reflective than paper. High reflectivity at high elevations is nearly universal on Venus and is thought to represent differences in chemical weathering of rocks at high and low elevations. Reflective stuff found at Atla, Ishtar, Beta. (iron pyrite -- fools good)
The left and center images are 90 x 180 kilometers, and the right image is 240 x 480 kilometers.
Reminder: Moon dark/light were visible images - indicate composition: dark (mare), light (cratered highlands)

## Slide 18
slope
pancake
domes
Venus

## Slide 19
roughness
lava flows
Venus

## Slide 20
reflectivity
Maxwell Montes
Venus

## Slide 21: InSAR uses phase

## Slide 22
Research with ALOS PALSAR data
within the WinSAR consortium
Matt Pritchard, Cornell (Chair)
and the WinSAR Executive Committee
Roland Burgmann, Yuri Fialko, Eric Fielding and David Schmidt
Outline of talk:
What is WinSAR ?
Research examples:
Earthquakes
Inter-seismic
Volcanoes
Subsidence
Others
Recommendations

## Slide 23
What is WinSAR ?
Consortium of 83 Universities/ Research Institutions (~20 non U.S.)
- Executive Committee (elected, 2-year terms)
- ALOS-PALSAR access through L1 data pool at ASF (U.S. Government Research Consortium, USGRC)
Funding:

## Slide 24
• Promote the use and development of InSAR technology for scientific investigations.
• Promote free and open access to SAR data as allowed by data providers.
Acquire, archive and catalog SAR data of the U.S. active areas
WinSAR objectives
Complete ERS,Envisat
data sets for core area!
# of scenes
ERS 22826 8.9 Tb
Envisat 7185 1.7 Tb
Nearly complete
ALOS-1 data set for North and South
America available at
ASF L1 Data Pool.

## Slide 25: Volcanic Hazards

## Slide 26
Yellowstone Caldera
ENVISAT IS1
Record one-year uplift using Space Based Geodesy
B = 231 m
2004/10/08 to 2005/09/23
C. Wicks, USGS
Notes: ENVISAT IS1 Track 048 (ascending). Orbits 13629 and 18639. NOAA’s NOHRSC website shows the ground bare of snow during each acquisition date.

## Slide 27
ENVISAT interferogram of Okmok volcano, Alaska, spanning 2003-2004. Located in the central Aleutian arc, Alaska, Okmok is a dominantly basaltic complex topped with a 10-km-wide caldera that formed circa 2.05 ka. Okmok erupted several times during the 20th century, most recently in 1997; eruptions in 1945, 1958, and 1997 produced lava flows within the caldera. Previous studies utilizing InSAR images from ERS-1, ERS-2, and Radarsat-1 sensors have shown that the inflation rate after the 1997 eruption generally decreased with time during 1997-2001, but increased significantly during 2001-2003. This recent interferogram shows continued inflation during 2003-2004 at a rate of about 60% that during 2002-2003. The InSAR image also shows post-emplacement deformation of the 1997 lava flow, most likely due to thermal contraction.
0
28 mm
5 km
N
unpublished data from Zhong Lu

## Slide 28
Averaged InSAR image from track 229 created by stacking all unwrapped 1-year interferograms from the 1992-2005 time period. The deformation histories for several points are shown for both track 229 and 501 interferograms. We attribute this deformation to thermoelastic contraction of the 1986 pyroclastic flow deposits. The graphs on the right side of the image give the deformation history for points 11, 16 and 17, which show a small amount of LOS shortening (5-6 cm) over the east flank of the Augustine Island. The graphs at the bottom of the image show little deformation on the south and west sides of Augustine Island. Blue lines are the best second-order polynomial fits to the observed LOS displacements.
Submitted for publication in Earth, Planets, and Space as:
Lee, C., Lu, Z. Kwoun, O., and Won, J., Deformation of Augustine Volcano, Alaska, 1992-2005, measured by ERS and ENVISAT SAR interferometry.

## Slide 29
inflation
subsidence
KILAUEA
MAUNA LOA
ENVISAT interferogram spanning November 2003 to January 2006 and showing inflation of the summits of Kilauea and Mauna Loa volcanoes, along with subsidence along both of Kilauea’s rift zones.
unpublished data from Mike Poland

## Slide 30: Kilauea - East Rift Zone, Dike Event June 17 - June 21, 2007
data from: http://www.soest.hawaii.edu/pgf/SEQ/

## Slide 31: Dike event - LOS ascending
Sandwell et al., 2008

## Slide 32: Earthquake Hazards

## Slide 33
Coseismic deformation of the Maule, Chile earthquake, ALOS-1
[Tong et al., 2010]
ScanSAR
provides second look direction

## Slide 34: Interseismic Deformation

## Slide 35
Line of sight
velocities from
stacked InSAR
data
35 interferograms
Epoch: 1992-2000
Fialko, Nature 2006
Southern
SAF

## Slide 36
Line of sight
velocities from
stacked InSAR
data
35 interferograms
Epoch: 1992-2000
Fialko, Nature 2006
Southern
SAF

## Slide 37
Western Salton trough 1992-2000
R. Mellors, SDSU
ERS 1,2 descending, 65 stacked interferograms

## Slide 38
Depth of slip
Superstition Hill fault
Creep is shallow and appears to occur primarily in the sedimentary section above the seismic zone.
(from Rob Mellors)
Fault zone behavior
basement
sediment
Depth of aseismic creep (1992-2000) on the Superstition Hill fault in comparison to microseismicity (red dots) and 1987 rupture (yellow).
From Lutz et al. 1987

## Slide 39
Schmidt et al., 2005, JGR
Year-To-Year
Seasonal
Uplift [mm]
Uplift [mm]
November 1998
March 1999
May 1999
September 1995
September 1997
September 1999
Schmidt and Bürgmann, 2003, JGR
Hilley et al., 2004, Science
Bürgmann, Pollitz et al.,2005 in prep., GRL
m = 6.7 x 1018 Pa s
LP
Ferretti et al., 2004
Ferretti et al., 2004, Eos
Notes: 49 ERS acquisitions from 1992 to 2000 were used to develop the permanent scatterer data set shown here. In addition to the plate-boundary strain evidenced by the (orange-to-blue) range-change gradient across the San Andreas fault system in the Bay Area, these data reveal (1) the distribution of aseismic slip and seismic potential of the Hayward fault and at San Juan Bautista, (2) the dynamics of aquifer deformation in the Santa Clara Valley, (3) rapid settling along the margins of San Francisco Bay, such as at Treasure Island, (4) dynamics of deep-seated landslides in the Berkeley Hills, and (5) the rheology of the upper mantle from postseismic relaxation following the 1989 Loma Prieta earthquake (evidenced by ≤ 2 mm/yr subsidence there).

## Slide 40: Hydrological Applications

## Slide 41
Annual groundwater recharge in LA Basin
(Watson et al., JGR 2001)
GPS Data

## Slide 42: Groundwater Pumping, Las Vegas
(Amelung et al., Geology, 1999)

## Slide 43
Oct 2001
Mar 2003
freeboard
added
Subsidence Measuring – Northeast Phoenix / North Scottsdale
decorrelated
(Buckley et al., 2003)

## Slide 44: InSAR Technology and Method

## Slide 45: Persistent scatterers
Long Valley Caldera,
Hooper et al. 2004

## Slide 46: Wide-swath InSAR
Bam earthquake
Rosen, 2006
Strip / ScanSAR InSAR
Bertran-Ortiz, 2007

## Slide 47: Atmospheric Corrections
From Foster et al., correction of Hawaii interferograms
Weather models can predict large-scale atmospheric signal

## Slide 48: Split-Beam Processing for 2-D
Split-beam processing yields 2-D vectors
Bechor, 2006

## Slide 49
SAR and InSAR Overview
atmosphere is very transparent to microwaves
radars measure range and azimuth
radar image has amplitude and phase
amplitude depends on roughness, slope, and dielectric constant.
phase differences reveal topography
phase differences reveal deformation
deformation from: volcanoes, earthquakes, groundwater
WInSAR has large archive of ERS, Envisat and ALOS data
Notes: 49