## Slide 1: Batch processing, stacking and time series analysis
Introduction
Batch processing
Stacking
Time series analysis
Xiaopeng Tong, InSAR workshop 2014, Boulder, CO

## Slide 2
Image alignment
Azimuth
Range

## Slide 3
Image alignment
Range
Azimuth
reference
repeat
Notes: The first step is to align the reference and repeat images to sub-pixel accuracy. This is done by two dimensional cross correlation of hundreds of small sub-patches (e.g., 64 x 64) taken from the master and slave images. Then a 6-parameter affine transformation is determined using a robust 2-D fit to the offset data.

## Slide 4
Aligned SAR data stacks

## Slide 5: Introduction
Batching processing: Automatic processing of a stack of SAR data to generate interferograms
Stacking: Average multiple interferograms to estimate velocity and standard deviations
Time-series analysis methods: SBAS, PSInSAR
Written in shell and is easy to modify so advanced users are welcome to develop new scripts

## Slide 6
standard deviation
combined high-resolution
velocity
[Tong et al., 2013]
ftp://topex.ucsd.edu/pub/SAF_models/insar/ALOS_ASC_masked.kmz
Notes: Say I will come back to it. Say you can say it’s really sharp along creeping section,

## Slide 7
Parkfield SAF
red 10 mm/yr
blue -10mm/yr

## Slide 8
Parkfield SAF
red 10 mm/yr
blue -10mm/yr

## Slide 9: Batch processing, stacking and time series analysis
Introduction
Batch processing
Stacking
Time series analysis
InSAR workshop 2014, Boulder, CO

## Slide 10: Overview
Batch processing:
  Preprocessing without a master image pre_proc_init.csh
  Preprocessing with a master image pre_proc_batch.csh
  Align a stack of SAR data align_batch.csh
  Form a stack of interferograms intf_batch.csh

## Slide 11: Batch processing: pre_proc_init.csh
Function:
  preprocess a stack of SAR data using default parameters (earth radius, Doppler centroid, near range)
  Generate baseline-time plot to choose master images, alignment strategy, interferometric pairs

## Slide 12: Batch processing: pre_proc_init.csh

## Slide 13
  Batch processing: pre_proc_init.csh

## Slide 14
Baseline-time plot: stacktable_all.ps

## Slide 15
Super master
Baseline-time plot: stacktable_all.ps

## Slide 16: Batch processing: pre_proc_batch.csh
Function:
  preprocess a stack of SAR data using uniform parameters (earth radius, Doppler centroid, near range) to make them geometrically consistent with one single image (super master)

## Slide 17: Batch processing: pre_proc_batch.csh
1. Modify data.in file
2. Delete old PRM and raw files
Super master

## Slide 18: Batch processing: pre_proc_batch.csh
3. Modify batch.config file and run pre_proc_batch.csh
Stop here to look at the batch.config file

## Slide 19: Batch processing: align_batch.csh
Function:
  Focus SAR images to form Single Look Complex (SLC) data
  Align (image registration) a stack of SLC data using 2D cross-correlation within sub-pixel (<10m) accuracy

## Slide 20
Baseline time plot
Super master

## Slide 21
master
slave
“Leap frog” method to align SAR images

## Slide 22
“Leap frog” method to align SAR images
Surrogate master
Slave

## Slide 23
“Leap frog” method to align SAR images

## Slide 24: Batch processing: align_batch.csh
Time-consuming part of the processing .. take a break here ..
1. Edit align.in file
Master or Surrogate master
Slave
Super master
2. Then run align_batch.csh

## Slide 25: Batch processing: intf_batch.csh
Function:
  Convert Digital Elevation Model into radar coordinates
  Form interferograms using two SLC data
  Remove phase due to earth curvature and topography
  Plot amplitude, correlation, phase using GMT
  Unwrap using SNAPHU
  Geocode and make Google Earth KML files

## Slide 26
Choose 3 interferograms pairs

## Slide 27: Batch processing: intf_batch.csh
1. Edit intf.in file to choose inteferogram pairs

## Slide 28: Batch processing: intf_batch.csh
2. Make dem.grd file and put it inside topo/ directory

## Slide 29: Batch processing: intf_batch.csh
3. Check/modify batch.config file
Time-consuming part of the processing .. take a break here ..

## Slide 30: Batch processing: results
All interferograms are in different folders in intf/
The folder can be named after either date or orbital number
  Modify batch.config to choose among date or orbital number
Each interferogram folder contains the following files:
  Amplitude, phase, correlation, unwrapped phase, filtered phase image files in GMT/NetCDF format “.grd”
  Corresponding files after geocoding with subfix “_ll.grd”
  Postscripts plots: “.ps”
  Google Earth “.kml” and “.png”

## Slide 31: Batch processing: results
Phase of the 3 interferograms

## Slide 32: Batch processing, stacking and time series analysis
Introduction
Batch processing
Stacking
Time series analysis (SBAS)
InSAR workshop 2014, Boulder, CO

## Slide 33: Stacking: stack_phase.bash
Function:
  Average unwrapped phase
  Convert the phase (radius) to velocity (mm/yr)
Note: it’s necessary to check the unwrapped phase before stacking or time-series analysis because unwrapping from SNAPHU may give errors, which will corrupt results
More complex processing techniques (e.g. filtering, detrending, GPS/InSAR integration) is incorporated along with stacking

## Slide 34
Math of stacking (Appendix C)
Unwrapped phase
Time span
atmosphere
topography
Recovered deformation
True deformation

## Slide 35
Stacking example with the complete data set

## Slide 36
Stacking example with the complete data set
Land subsidence near Coachella Valley, California
Track 213 Frame 660

## Slide 37: Batch processing, stacking and time series analysis
Introduction
Batch processing
Stacking
Time series analysis (SBAS)
InSAR workshop 2014, Boulder, CO

## Slide 38
Since 2006/01/01
T213 F660 ALOS
SBAS
88 interferograms
28 scenes
20 km filter

## Slide 40: Time-dependent deformation signals

## Slide 41: Time-series show seasonal variation and linear trend
Point B
Point A

## Slide 42: Summary
Batch processing shell scripts provide automatic InSAR data processing
Stacking scripts provide methods to estimate mean velocity and its standard deviations.
Advanced user can develop custom scripts using tools inside GMT and GMTSAR.
InSAR time-series analysis tool has been developed and will be in the next version of GMTSAR.
Any questions?