UNAVCO POLAR RECEIVER CONFIGURATION FORM

Receiver			TRIMBLE NETR9

Firmware			4.93

Config. Form Version 	1.0

Date			 	March 11, 2015

Project / Network

System ID

Configured by

Upon completion this hardcopy is placed in network folder with the Polar Network Engineer.

TRIMBLE NETR9

| Date |  |
| --- | --- |
| UNAVCO ID |  |
| Serial Number |  |

| SETTING | POLAR DEFAULT | ACTUAL |
| --- | --- | --- |

Commonly modified settings are shown in RED Italics.

Receiver Status

Identity

| System Name | NAME |  |
| --- | --- | --- |

Receiver Options

| Firmware Warranty Date | 5 years from purchase |  |
| --- | --- | --- |
| L2E Tracking installed | Yes |  |
| L2C Tracking installed | Yes |  |
| Data Logging installed | 4GB |  |
| Prog. Interface installed | Yes |  |

Satellites

GPS Enable/Disable

| Enable | All checked |  |
| --- | --- | --- |
| Ignore Health | All NOT checked |  |

SBAS Satellite Enable/Disable

| Setting | All Off |  |
| --- | --- | --- |

Data Logging

File System /Internal

| Size | 4GB |  |
| --- | --- | --- |
| Available | 3.9GB approx.. |  |
| Autodelete | NOT checked |  |

File System /External (only if a 4GB USB thumb drive is installed)

| Size | 4GB |  |
| --- | --- | --- |
| Available | 3.9GB approx.. |  |
| Autodelete | NOT checked |  |
| Session DEFAULT | Disabled |  |
| Session 1hr_30s | Enabled |  |
| Session Name | 1hr_30s |  |
| Enable | Checked |  |
| Schedule | Continuous |  |
| Duration | 60 Minutes |  |
| Measurement Interval | 30 sec. |  |
| Smooth Pseudorange | NOT Checked |  |
| Smooth Phase | NOT Checked |  |
| Include Doppler | NOT Checked |  |
| Position Interval | 10 Min. |  |
| Log Received Corrections | NOT Checked |  |
| Log Raw Nav Data | NOT Checked |  |
| Log SBAS Data | NOT Checked |  |
| File System | /Internal |  |
| Path Style | YYYYMM/DD |  |
| Name Style | SystYYYYMMDDHHmm |  |
| Suffix | A |  |
| Pool | Delete When Full |  |
| Pool | 1900MB |  |
| NOTE with these settings the NetR9 will write files until the disk fills to this amount. At that point it will delete the oldest files to maintain free disk space. NOTE new stations are set to Stop When Full. |
| FTP Push | Off |  |
| Email Push | NOT Checked |  |

| Session 24hr_int | Enabled |  |
| --- | --- | --- |
| Session Name | 24hr_int |  |
| Enable | Checked |  |
| Schedule | Continuous |  |
| Duration | 1440 Minutes |  |
| Measurement Interval | 30 sec. |  |
| Smooth Pseudorange | NOT Checked |  |
| Smooth Phase | NOT Checked |  |
| Include Doppler | NOT Checked |  |
| Position Interval | 10 Min. |  |
| Log Received Corrections | NOT Checked |  |
| Log Raw Nav Data | NOT Checked |  |
| Log SBAS Data | NOT Checked |  |
| File System | /Internal |  |
| Path Style | YYYYMM/DD |  |
| Name Style | SystYYYYMMDDHHmm |  |
| Suffix | B |  |
| Pool | Delete When Full |  |
| Pool | 1900MB |  |
| NOTE with these settings the NetR9 will write files until the disk fills to this amount. At that point it will delete the oldest files to maintain free disk space. NOTE new stations are set to Stop When Full. |
| FTP Push | Off |  |
| Email Push | NOT Checked |  |
| Session 24hr_ext | Enabled |  |
| Session Name | 24hr_ext |  |
| Enable | Checked |  |
| Schedule | Continuous |  |
| Duration | 1440 Minutes |  |
| Measurement Interval | 30 sec. |  |
| Smooth Pseudorange | NOT Checked |  |
| Smooth Phase | NOT Checked |  |
| Include Doppler | NOT Checked |  |
| Position Interval | 10 Min. |  |
| Log Received Corrections | NOT Checked |  |
| Log Raw Nav Data | NOT Checked |  |
| Log SBAS Data | NOT Checked |  |
| File System | /External |  |
| Path Style | YYYYMM/DD |  |
| Name Style | SystYYYYMMDDHHmm |  |
| Suffix | C |  |
| Pool | Delete When Full |  |
| Pool | 3900MB |  |
| NOTE with these settings the NetR9 will write files until the disk fills to this amount. At that point it will delete the oldest files to maintain free disk space. NOTE new stations are set to Stop When Full. |
| FTP Push | Off |  |
| Email Push | NOT Checked |  |

Power Saving

| Power Off When Not Logging | NOT Checked |  |
| --- | --- | --- |

RINEX Header Info

| Observer Name | UNAVCO |  |
| --- | --- | --- |
| Agency Name | UNAVCO |  |
| FTP Push | N/A |  |

Receiver Configuration

Antenna

| Antenna Type |  |  |
| --- | --- | --- |
| RINEX Name |  |  |
| Antenna Serial Number |  |  |
| Radome Serial Number |  |  |
| Antenna Measurement Method |  |  |
| Antenna Height (m) |  |  |
| Apply Antenna Correction RTCM V3 | NOT Checked |  |

Reference Station

| RTCM 2.x ID | N/A |  |
| --- | --- | --- |
| RTCM 3.x ID | N/A |  |
| Station Name | NAME |  |
| All Other Options | N/A |  |

Tracking

| Elevation Mask | 7 |  |
| --- | --- | --- |
| Everest | Disable |  |
| Clock Steering | Enable |  |
| GPS L1-CA Enable | Checked |  |
| GPS L2E Enable | Checked |  |
| GPS L2E Options | L2C and L2E |  |
| GPS L2C Enable | Checked |  |
| GPS L2C Options | CM + CL |  |
| GPS L5 Enable | NOT Checked |  |
| SBAS L1 – C/A Enable | NOT Checked |  |
| SBAS L5 Enable | NOT Checked |  |
| Correction Controls | N/A |  |

Position

| PDOP Mask | 99 |  |
| --- | --- | --- |
| All Other Options | N/A |  |

General

| External Frequency | Disable |  |
| --- | --- | --- |
| 1 PPS On/Off | Disable |  |
| Internal Battery UPS | Disable |  |
| UPS Timeout (seconds) | 35 |  |
| Battery Charging Mode | When ON |  |
| Battery Charging Voltage | Programmable |  |
| Battery Charging Minimum | 13.00 Volts |  |
| Power Over Ethernet | Disable |  |
| Ethernet Battery Charging | Disable |  |
| Power On Voltage | 12.50 Volts |  |
| Shutdown Voltage | Enable |  |
| Shutdown Voltage | 10.50 Volts |  |
| NOTE 10.50 Volts is setting when powering NetR9 through an 11.0V LVD 11.00 Volts is setting when powering NetR9 directly from batteries |
| Shutdown Override | Disable |  |
| VFD Configuration | Enable |  |
| VFD Power Saver | Enable |  |
| Power Saver Timeout (seconds) | 60 |  |
| VFD Suppress Warming Msg. | Enable |  |
| VFD Brightness | 25% |  |
| VFD Rotation | Disable |  |
| Application Files | Create, download and save clone file after configuration complete. See end of form. |
| Reset | N/A |  |
| Default Language | English |  |

| I/O Configuration | N/A |  |
| --- | --- | --- |

OmniSTAR

Configuration

| Preferred Source of Data | N/A |  |
| --- | --- | --- |
| External OmniSTAR Data | Don’t Use |  |
| All Options | N/A |  |

Network Configuration

Ethernet

| IP Setup | Static IP |  |
| --- | --- | --- |
| IP Address | 192.168.1.2 |  |
| Netmask | 255.255.255.0 |  |
| Gateway | 192.168.1.1 |  |
| Hostname | N/A |  |
| MTU | 1500 |  |

DNS Configuration

| Force DNS Address | NOT Checked |  |
| --- | --- | --- |
| DNS Address | N/A |  |
| Sec DNS Addr | N/A |  |
| DNS Domain | N/A |  |
| DNS Proxy | N/A |  |
| PPP | N/A |  |

Routing Table

| Change Default Route | N/A |  |
| --- | --- | --- |
| Add a Route | N/A |  |
| Network Address Translation | Disable |  |
| IP Filtering Enable | N/A |  |
| RTPD Server | N/A |  |
| E-mail Client | N/A |  |
| E-mail Alerts |  |  |
| Enable | NOT Checked |  |
| To E-Mail Address | N/A |  |
| All Options | N/A |  |
| HTTP |  |  |
| HTTP Enable | Checked |  |
| HTTP Server Port | 80 |  |
| HTTP Secure Enable | Checked |  |
| HTTP Secure Port | 443 |  |
| Proxy |  |  |
| Enable HTTP Proxy | NOT Checked |  |
| FTP |  |  |
| FTP Server Enable | Checked |  |
| FTP Server Port | 21 |  |
| Configure TCC | N/A |  |
| NTP |  |  |
| External Time Servers | N/A |  |
| Enable NTP Client | NOT Checked |  |
| Enable NTP Server | NOT Checked |  |
| Reference Clock Offset | N/A |  |
| VFD |  |  |
| Enable | NOT Checked |  |
| VFD Server Port | N/A |  |
| DDNS Client |  |  |
| Enable | NOT Checked |  |
| All Options | N/A |  |
| Zeroconf/UPnP |  |  |
| Enable Zeroconf service… | NOT Checked |  |
| Enable UPnP service discovery | NOT Checked |  |
| Forward HTTP | NOT Checked |  |
| Forward FTP | NOT Checked |  |
| Forward IO | None |  |

Security

Configuration:

| Security | Disabled |  |
| --- | --- | --- |
| All Options | N/A |  |

Firmware

Install:

| Active Firmware Version | 4.93 |  |
| --- | --- | --- |
| FW Upgrade Check |  |  |
| Enable | NOT Checked |  |

| Programmatic Interface | N/A |  |
| --- | --- | --- |

Note: Programmatic Interface should be activated on all NetR9. If it is not, a code will be needed to activate it.

| Create Clone File | Filename |  |
| --- | --- | --- |

Include system name and date in filename, i.e. NAME_2015-03-11.xml

| Download and save Clone File |  |  |
| --- | --- | --- |