UNAVCO Polar Remote Site Visit Procedures		Version 1.0, December 21 2012

REPLACING GPS BOARD

REMOVE OLD BOARD:

Turn off all breakers

Power down GPS with power button

Unplug all connectors from enclosure wall and remove red/black wires from battery bank

Remove SIM cards from dial-up modems(s) and keep in safe place

Remove board from enclosure

INSTALL NEW BOARD:

Record UID for 				GPS Receiver  -  Primary Iridium modem  -  Secondary Iridium modem

Record timer switch settings 		(typical 1000m / 1000m for dual, 1000m / 10m for single)

Verify all breakers off (green showing)

Verify GPS power plug(s) disconnected

Place new board into enclosure

Place regulator temp sensors on batteries

Connect all cables to enclosure wall	Power, Met, GPS antenna, Iridium antenna(s)

Connect heat pads to terminal blocks

Connect red/black wires to battery bank

Check and record voltages		(see MEASURING VOLTAGES section)

Turn on all breakers (red showing)

Check regulators:			Solar charge LED:  	green, or red with green flash

Solar LVD LED: 	green (magnet to reset if red)

Wind charge LED:  	green, or red with green flash

Battery voltage: 	voltage increasing?

Plug in GPS power cable(s)

Verify GPS front panel operating normally

IF Xeos modem: 			Perform Xeos checks	(see IRIDIUM CHECKS section)

IF single dial-up modem: 		Install SIM into modem

IF dual dial-up modems:			Load breaker OFF

Install active SIM into secondary modem

Load breaker ON

Place test call to secondary modem    (see IRIDIUM CHECKS section)

Load breaker OFF

Move active SIM to primary modem

Install backup SIM inside secondary modem

Load breaker ON

Photograph GPS board

Place foam cap over electronics

Slide board into anti-static bag, attach alligator clip leads from bag to system ground

Verify ground wires connected from enclosure ground plate to battery negative

Photograph inside of enclosure AND connectors on enclosure wall

Verify all breakers still ON

Close, latch, and strap all enclosures

Place test call to primary modem	(see IRIDIUM CHECKS section)

REPLACING A GPS RECEIVER

Power down old receiver with power button

Remove all connectors from rear panel of receiver and remove receiver from board

Install new receiver and reconnect all connectors to rear panel

TRIMBLE NETRS					TRIMBLE NETR9

Power A  	to dongle				Power 2	7-pin LEMO (be careful)

Ethernet 	to dongle (for Xeos or radio only)	Ethernet	(for Xeos or radio only)

Power B 	lock this connector			USB		with 4GB external drive

Serial 2 	primary dial-up Iridium			Serial 2		Met station

Serial 3 	Met station if secondary Iridium used	Antenna cable	to type N connector on enclosure wall

Serial 4 	secondary Iridium, otherwise Met

Antenna cable	to type N connector on enclosure wall

Verify GPS operation from front panel

TRIMBLE NETRS		   			TRIMBLE NETR9

Satellite:   	red 1Hz		   			Lower Left:	Logging / USB

Data:       	yellow 1Hz	  			Upper Left:	SV X    (X>5)

Power A:  	solid green	   			Upper Right:	Battery icon

Power B: 	solid yellow

Record UID of new receiver

REPLACING A DIAL-UP IRIDIUM MODEM

Turn off load breaker (yellow wires)

Remove Iridium modem and its power / serial cable

Move SIM card to new modem

Install new modem and power / serial cable

Serial cable		To NetRS serial 2 (primary) or serial 4 (secondary)

Iridium positive lead 	To timer switch pin 1

Iridium negative lead	To timer switch pin 3

Coaxial antenna cable	To type TNC connector on enclosure wall

Turn on load breaker

Record UID of new Iridium modem

REPLACING AN IRIDIUM ANTENNA

Unplug the old cable from the enclosure and remove all cable ties from frame

Remove old antenna and cable

Install new antenna and cable. Hand tighten the TNC connector then use pliers to tighten further.

Route cable back to enclosure and plug in. NO SHARP BENDS OR KINKS IN THIS CABLE

Anchor cable with a tie every ~18", taking care to avoid sharp edges

REPLACING A WEATHER STATION

Unplug the old cable from the enclosure and remove all cable ties from frame

Remove weather station by unscrewing small set screw inside base of weather station

Install new weather station on frame

Orient the new weather station so its "north" arrow on bottom points toward true north

Route cable back to enclosure and plug in

Anchor cable with a tie every ~18", taking care to avoid sharp edges

Record UID of new weather station

Record height of weather station above/below (+/-) GPS antenna

REPLACING A SOLAR PANEL

Unplug the old cable from the enclosure and remove all cable ties from frame

Unscrew 4 saddle clamps from frame and remove panel

Install new panel using 4 saddle clamps

Route cable back to enclosure and plug in

Anchor cable with a tie every ~18", taking care to avoid sharp edges

REPLACING A WIND TURBINE

Unplug the old cable from the enclosure and remove all cable ties from frame.

Remove wind turbine from frame.

Install new turbine on frame.

Route cable back to enclosure and plug in.

Anchor cable with a tie every ~18", taking care to avoid sharp edges.

IRIDIUM CHECKS

TEST CALL TO NETRS THROUGH DIAL-UP MODEM

Connect Iridium handset to laptop serial port. Power the handset and extend antenna vertically.

Make sure you have good sky view for the antenna

Open previously configured Iridium dial-up Network Connection.

Enter Iridium phone number and click Dial. May take several tries. If persistent failures:

Phone number correct?

Active SIM card installed on remote modem?

Remote Iridium modem on?

Remote modem antenna cable and connectors OK?

Breakers on?

After "Registering Computer On Network" box disappears, connection has been made to GPS

In any browser, enter following commands (xx = unique for each remote station)

Note: your computer will be 192.168.xx.1. See this IP under Dial-Up in the Network Connections window.

http://192.168.xx.2/prog/show?systemname		Verify you have connected to the right site

http://192.168.xx.2/prog/show?serialnumber		Record on checklist

http://192.168.xx.2/prog/show?firmwareversion		Running 1.3-2 (or 1.3-1 or 1.3-0). Record on checklist.

http://192.168.xx.2/prog/show?voltage&input=1		Voltage 1 is >13V and charging

http://192.168.xx.2/prog/show?voltage&input=2		Voltage 2 is >13V and charging

http://192.168.xx.2/prog/show?loggingstatus		Verify NetRS is logging 60-minute datafile

http://192.168.xx.2/prog/show?trackingstatus		Must have nonzero L1snr and L2snr values

CHECKS WITH XEOS MODEM

Upon power up, Power LED flashes then solid yellow 		<10 seconds

Press DAS Test button. DAS OK LED flashes then solid yellow. 	Verifies Ethernet connection to GPS. <20 seconds.

Press SAT Test button. SAT OK LED flashes then solid yellow 	Verifies Iridium link (up to 90 sec). May take 2-3 tries.

Note: Xeos goes to sleep after 15 minutes. 			If asleep, cycle load breaker to wake up.

MEASURING VOLTAGES

TURN ALL BREAKERS OFF

BATTERY VOLTAGES (with breakers OFF)

Verify voltmeter is set to measure DC voltage (NOT DC current).

If no individual breakers for auxiliary battery banks:

Unplug all external battery cables from outside of enclosure

Measure main bank voltage from port 2 on battery breaker to black terminal blocks

Measure auxiliary bank voltages at external battery cable (pin B positive)

Reconnect external battery cables to enclosure

If individual breakers for auxiliary battery banks:

Measure main bank voltage from port 2 on main battery breaker to black terminal blocks

Measure auxiliary bank voltages from port 2 on auxiliary battery breakers to black terminal blocks

All battery voltages should be steady ≥13V if system charging on arrival.

All battery voltages should be steady <13V if system not charging on arrival.

SOLAR PANEL VOLTAGES (with breakers OFF)

Unplug all but one panel from outside of box.

Measure solar panel voltage from port 2 on solar breaker (orange wires) to black terminal blocks.

Should be >20V

Unplug first panel. Connect second panel into different plug.

Measure voltage again.

Repeat for panels 3 and 4 if necessary.

Reconnect all panels to enclosure.

WIND TURBINE VOLTAGES (with breakers OFF)

Unplug all but one turbine from outside of box.

Measure wind turbine voltage from port 2 on wind breaker (blue wires) to black terminal blocks.

Should be >15V when spun by hand

Unplug first turbine. Connect second turbine into different plug.

Measure voltage again.

Reconnect both turbines to enclosure.

HEAT PAD RESISTANCE (with breakers OFF)

Set voltmeter to resistance.

Measure purple to black blocks.

Should be ~7ohms when cold.

TURN ALL BREAKERS ON

LOAD VOLTAGE (with breakers ON)

Measure load voltage from yellow terminal blocks to black terminal blocks.

Should equal battery voltage.