## Slide 1
GPS Data and Earthquake Hazard Original activity design by Roger Groom and Robert Butler. Modifications by Beth Pratt-Sitaula. Some slides contributed by Vince Cronin.
Version May 26, 2013

## Slide 2
GPS receiver
Notes: This is a handheld GPS unit that has been available to the public for more than a decade now and is often used for hiking or other outdoor activities.

## Slide 3
GPS receiver
Notes: Whether they know it or not, students use GPS receivers daily in their cars, phones, cameras, and more. Most have heard the term “GPS” but few know much about how the system actually works or high precision GPS for science and industrial use.

## Slide 4
GPS receiver
Notes: Whether they know it or not, students use GPS receivers daily in their cars, phones, cameras, and more. Most have heard the term “GPS” but few know much about how the system actually works or high precision GPS for science and industrial use.

## Slide 5
The Global Positioning System
24-32 satellites
20,200 km altitude
55 degrees inclination
12 hour orbital period
5 ground control stations
Need 4 satellites to be accurate
Each satellite passes over a ground monitoring station every 12 hours
Notes: From the users point of view, GPS is a passive system: you need only a low-powered receiver to obtain the signals, which contain all the information you need to determine your position. This requires that the satellites carry atomic clocks to keep accurate time and transmit to the user the position of the satellite in the sky. The orbits are computed by Department of Defense (DoD) by tracking the satellites at five ground Master Control Monitoring stations with known positions and then uploaded to the satellites which then transmit the information continuously along with the time. With hand-held receivers, it is possible to find your position to a few meters, limited primarily by the accuracy of the broadcast orbits. As we shall see, the civilian scientific community uses over 200 stations to determine the orbits with an accuracy of a few centimeters, allowing millimeter positioning with after several hours of tracking.

## Slide 6
Consumer-grade GPS accuracy
Horizontal: +/- 10 m (30 ft) error
Vertical: +/- 15 m (45 ft) error
Your location is:
37o 23.323’ N
122o 02.162’ W
Notes: Since each satellite maintains time very accurately (~1 nanosecond = 30 cm), it can tag its signal with the time of transmission. This information, together with the location of the satellite, also transmitted to the receiver, is sufficient to allow the receiver to calculate the range to each satellite provided that the receiver also knows also knows the time. Equipping receivers with atomic clocks would be very expensive, so the receiver tags the signal with the time of its internal clock to create a “pseudorange” (range plus an unknown clock correction). The software in the receiver than uses the pseudoranges from four satellites to solve for the four unknowns: three coordinates and the receiver clock correction.

## Slide 7: Anatomy of a High-precision Permanent GPS Station
GPS antenna inside of dome
Monument solidly attached into the ground with braces.
If the ground moves, the station moves.
Solar panel for power
Equipment enclosure
GPS receiver
Power/batteries
Communications/ radio/ modem
Data storage/ memory
Notes: Example of a typical remote GPS station. In urban areas, some are also fixed to the roof of large reinforced buildings and hooked into grid power supply with battery backup. Many stations are now being equipped with “real time” communication to allow immediate transfer of data to researchers. In other places logistics or country-specific regulations require that data not be transmitted but is instead downloaded manually on a given schedule (monthly, quarterly, annually depending on the site)

## Slide 8
High-precision GPS
Current accuracies of few millimeters per year
Stable monuments
Sophisticated processing software
Ability to use additional satellite information
Long measurement times
Notes: High precision GPS operate in essentially the same way as regular consumer GPS but due to a variety of factors including stable monuments, use the satellite signal carrier phase, dual-frequency receivers, high-precision orbital information, stable monuments, multiple stations, sophisticated processing, and long measurements times, these station are able to achieve accuracies of 1-2 mm/yr in many situations.

## Slide 9
Reading GPS data
Station position over time
  North-South
  East-West
  Up-Down
Notes: P401-Quillayut station is located in the town of Forks on the Olympic Peninsula of Washington State.
ALL DATA IN THIS ACTIVITY WERE ACQUIRED FROM http://pbo.unavco.org/data/gps
The data are “raw” position files in the Stable North American Reference Frame (SNARF) (for more on reference frames see http://facility.unavco.org/data/maps/GPSVelocityViewer/GPSVelocityViewer-frames.html_

## Slide 10
Reading GPS data
From the changing position velocity can be calculated using SLOPE (rise-over-run)
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
6 – (-63) = 69 mm
2013.4 – 2005.25 = 8.15 years
69 mm / 8.15 years = 8.5 mm/yr
Notes: Using just the North-south data, you can run through how to estimate station velocity in this direction by using the simple, graphical method of rise-over-run to determine slope.
Students will have to be comfortable with estimating as best they can from the axes scales – Y axis more so due to fewer tick marks
Zero point is arbitrary. Relative location is important. (In older PBO time series the zero was often set to the average position over the data interval
PLEASE NOTE: the velocity estimates presented in this activity are NOT the official ones published by PBO but those likely to be determined graphically using data through May 2013. However, the graphically-measured velocities are quite representative of the published ones and completely sufficient for class discussions regarding accumulating strain and earthquake hazard.

## Slide 11
Reading GPS data
Repeat process for east-west movement
69 mm / 8.15 years = 8.5 mm/yr
120 mm / 8.15 years = 14.7 mm/yr
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Using just the North-south data, you can run through how to estimate station velocity in this direction by using the simple, graphical method of rise-over-run to determine slope.
Students will have to be comfortable with estimating as best they can from the axes scales – Y axis more so due to fewer tick marks

## Slide 12
Quillayut, WA GPS Velocity
13
14
17.0 mm / yr
Notes: At this point you can have your students simply use a graphical measurement (using paper with tick marks to measure) to determine the hypotenuse measurement of the total horizontal velocity OR you can remind of the Pythagorean method: sqrt(a^2 + b^2) = hypotenuse

## Slide 13
GPS Stations in Cascadia
Newport
Corvallis
Tillamook
Pacific
Beach
Neah
Bay
Kelso
Tumwater
Othello
La Grande
Wasco

## Slide 14
Neah Bay, WA GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Station NEAH

## Slide 15
Neah Bay, WA GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
68 mm / 9.4 yr = 7.2 mm/yr
105 mm / 9.4 yr = 11.2 mm/yr
Notes: Station NEAH

## Slide 16
13.3 mm / yr
Neah Bay, WA GPS Velocity
Notes: At this point you can have your students simply use a graphical measurement (using paper with tick marks to measure) to determine the hypotenuse measurement of the total horizontal velocity OR you can remind of the Pythagorean method: sqrt(a^2 + b^2) = hypotenuse

## Slide 17
Pacific Beach, WA GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Station PABH

## Slide 18
Pacific Beach, WA GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
100 mm / 59.4 yr = 10.6 mm/yr
125 mm / 9.4 yr = 13.5 mm/yr
Notes: Station PABH

## Slide 19
Pacific Beach, WA GPS Velocity
13
14
17.2 mm / yr

## Slide 20
Tillamook, Oregon GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Station CHZZ
Note: station antenna was shot by vandals in 2010 and had to be replaced leading to a slight offset in the data

## Slide 21
Tillamook, Oregon GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
73 mm / 9.4 yr = 7.8 mm/yr
75 mm / 9.4 yr = 8.0 mm/yr
Notes: Station CHZZ
Note: station antenna was shot by vandals in 2010 and had to be replaced leading to a slight offset in the data

## Slide 22
11.1 mm / yr
Tillamook, Oregon GPS Velocity

## Slide 23
Newport, OR GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Station P367
Note: this station has a different start date than most in this exercise!

## Slide 24
Newport, OR GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
54 mm / 6.3 yr = 8.6 mm/yr
44 mm / 6.3 yr = 7.0 mm/yr
Notes: Station P367
Note: this station has a different start date than most in this exercise!

## Slide 25
11.1 mm / yr
Newport, OR GPS Velocity

## Slide 26
Tumwater, WA GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Station TWHL

## Slide 27
Tumwater, WA GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
40mm / 9.4 yr = 4.3 mm/yr
54 mm / 9.4 yr = 5.7 mm/yr
Notes: Station TWHL

## Slide 28
7.1 mm / yr
Tumwater, WA GPS Velocity

## Slide 29
Kelso, WA GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Station P446

## Slide 30
Kelso, WA GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
30 mm / 5.1 yr = 5.3 mm/yr
31 mm / 5.1 yr = 5.4 mm/yr
Notes: Station P446

## Slide 31
7.6 mm / yr
Kelso, WA GPS Velocity

## Slide 32
Corvallis, Oregon GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Station CORV

## Slide 33
Corvallis, Oregon GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
57 mm / 9.4 yr = 6.1 mm/yr
43 mm / 9.4 yr = 4.6 mm/yr
Notes: Station CORV

## Slide 34
7.6 mm / yr
Corvallis, OR GPS Velocity

## Slide 35
Othello, WA GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Station P451

## Slide 36
Othello, WA GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
6 mm / 8.4 yr = 0.7 mm/yr
7 mm / 8.4 yr = 0.8 mm/yr
Notes: Station P451

## Slide 37
1.1 mm / yr
Othello, WA GPS Velocity

## Slide 38
Wasco, OR GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Station P445

## Slide 39
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
16 mm / 7.6 yr = 1.8 mm/yr
7 mm / 7.6 yr = 0.9 mm/yr
Wasco, OR GPS Data
Notes: Station P445

## Slide 40
1.8 mm / yr
Wasco, OR GPS Velocity

## Slide 41
La Grande, OR GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
Notes: Station P022

## Slide 42
La Grande, OR GPS Data
2006
2007
2008
2004
2005
2009
2010
2011
2012
2013
2014
3 mm / 8 yr = 0.4 mm/yr
-2 mm / 8 yr = -0.3 mm/yr
Notes: Station P022

## Slide 43
-0.5 mm / yr
La Grande, OR GPS Velocity
-1
1
2
3
4
5
6
7
8
9
10
11

## Slide 44: GPS velocities
Newport
Corvallis
Tillamook
Pacific
Beach
Neah
Bay
Kelso
Tumwater
Othello
La Grande
Wasco

## Slide 45
Notes: Extra in case you wish to make any more graphs for specific other stations.

## Slide 46
13
14