# GPS Base Station AMU2

Amundsen-Scott South Pole Station Antarctica

Station Operating Procedures and Inventory

Version 2.4: December 2012

1.	 OPERATING PROCEDURES

1.1	Contact Information

Site operation is performed by UNAVCO event T-295, in conjunction with USGS event G-052. Contacts are:

UNAVCO:

Support email (will reach polar personnel)	support@unavco.org

USGS:

Team Leader, Geodesy	 Larry Hothem 	ldhothem@gmail.com, Lhothem@usgs.gov

Principal Investigator	Jerry Mullins 	Jmullins@usgs.gov

1.2	Normal Operation

GPS Base Station AMU2 is comprised of a Trimble NetR8 GPS receiver, an Ashtech choke ring antenna with radome, an Efratom rubidium frequency standard with power supply, a Wenzel frequency doubler, a 1x8 GPS antenna splitter, and associated power, Ethernet, and RF cabling. Spare components are located in the USGS cabinet nearby. As of 2012 this system falls under the domain of the station Aurora Tech Research Associate (RA).

NOTE: the GPS antenna is bolted to the roof of the elevated station via a short mast.

This antenna should never be disturbed, shadowed, or moved.

The Trimble NetR8 should have the following on its front panel display (press any button to illuminate display). We ask that these be checked occasionally, about once per week.

SV X 			(where X is a number greater than 5)

Ref Stn / Logging 	(alternating)

Battery icon		(should be full)

No other regular action is required. Data download, configuration changes, firmware upgrades, etc. are handled remotely by UNAVCO.

The GPS receiver, GPS antenna splitter, frequency standard, and frequency doubler should be powered by UPS. The NetR8 receiver also has its own internal battery which functions as a UPS for about 8 hours if external power is lost.

1.3	Swapping Components

No system components are user-serviceable, however an inventory of spares for most items is maintained in the USGS cabinet next to the GPS base station. If replacement is needed, UNAVCO will contact the RA and provide instructions. Also, UNAVCO personnel deploy to McMurdo Station each summer season, and are available for assistance.

1.4	Online Access and Data Download

Occasionally, there may be need for visiting science groups or the RA to access the receiver online and/or download data. The receiver has a web interface at 157.132.24.30 and is accessible from the South Pole network.

To download data, use any web browser and enter the above IP address. On the left side menu of the Trimble NetR8 web interface, click Data Logging then Data Files, and navigate to the desired file. To download a file, simply click on the filename.  When prompted for login information, use the login/password amu2/gps. This account allows data download only (there is a separate account for receiver control). As of December 2012 the receiver is logging data in three separate sessions:

15 second (“low-rate”) data is logged to 24-hour files named

AMU2YYYYMMDD0000A.T01

These files are stored in directories named

/Internal/YYYYMM/24hr15sc/

This data is downloaded and archived daily by UNAVCO. 1000MB memory is allocated on the receiver for storage of this data (2 years worth), with the oldest files being deleted once full.

2 Hz (“high-rate”) data is logged to 1-hour files, stored in daily directories named

AMU2YYYYMMDDHH00B.T01

These files are stored in directories named

/Internal/YYYYMM/DD/1hr2hz/

This data is downloaded and archived by UNAVCO during the austral summer season, but only by request during other times of the year. If high-rate data is required an email request should be sent to support@unavco.org. 1000MB memory is allocated on the receiver for storage of this data (40 days worth), with the oldest files being deleted once full.

10 Hz (“high-rate”) data is logged to 1-hour files, stored in daily directories named

AMU2YYYYMMDDHH00C.T01

These files are stored in directories named

/Internal/YYYYMM/DD/1hr10hz/

This data is NOT downloaded or archived by UNAVCO except by request. If high-rate data is required an email request should be sent to support@unavco.org. 1000MB memory is allocated on the receiver for storage of this data (9 days worth), with the oldest files being deleted once full.

The receiver’s IP settings are:

Static IP:   157.132.24.30

Gateway:  157.132.24.1

Netmask:  255.255.255.0

In the event that there is a need for station personnel to modify these or any other receiver settings, UNAVCO will provide instructions and/or the required login info.

2.	INVENTORY OF STATION EQUIPMENT AND SPARES

# Table 1 -- Components of the AMU2 GNSS system

| Quantity | Manufacturer and/or Description | Model | Serial Number | Owner | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1 | Trimble GPS Receiver | NetR8 | UNAVCO # 28930 S/N 5010K66018 | UNAVCO | “Primary” GPS receiver |
| 1 | Trimble 3-way power/download cable (LEMO / serial / coax power) | -- |  | UNAVCO |  |
| 1 | Ethernet cable (NetR8 receiver to wall jack) | -- |  | UNAVCO |  |
| 1 | Trimble Power Supply, AC to 18VDC | SDA5518 |  | UNAVCO |  |
| 1 | BNC T splitter | -- |  | UNAVCO | Split 5 MHZ signal from the Rubidium Oscillator |
| 1 | Ashtech Dorne Margolin choke ring antenna | -- | CR13569 | USGS | P/N 700936D |
| 1 | Radome cover for antenna | SCIGN |  | USGS |  |
| 1 | Efratom Rubidium Oscillator | -- | 9573 | NGA | 5 MHZ output |
| 1 | Power supply for rubidium oscillator | A24mT210 |  | USGS | Acopian regulated power supply |
| 1 | APC UPS | Pro BP650S | NB0023261597 | USGS | Powers frequency doubler and GPS antenna splitter |
| 1 | APC UPS | 280 |  | USAP NSF # 051615 | Powers GPS receiver and rubidium oscillator power supply |
| 1 | GPS Source Antenna Splitter | S18 |  | UNAVCO | 1x8 N type connectors; splitter also provides GPS for timing to Stanford VLF/ELF and Maryland DAS systems. |
| 1 | Antenna cable, N-N type connectors, length approximately 15 meters. | -- |  | USGS | From antenna splitter to D-M Choke Ring antenna located on roof above Science Laboratory |
| 1 | GPS Source GPS antenna splitter 8-to-1 | S18 |  |  |  |
| 1 | Cable with BNC connectors, short length | -- |  | UNAVCO | From BNC T-splitter on the Rubidium Oscillator to NetR8 GPS receiver |
| 1 | Antenna cable, N-N type connectors, short length | -- |  | UNAVCO | From antenna splitter to the NetR8 antenna signal input |
| 1 | Wenzel Assoc. Frequency Doubler; 5 to 10 MHz | LNHD-5-10 | 15882-0551 | UNAVCO | Provide 10 MHz input to NetR8 from Rubidium 5 MHz output |

Table 2 -- Accessories and Spare Parts

| Quantity | Manufacturer and/or Description | Model | Serial Number | Owner | Remarks |
| --- | --- | --- | --- | --- | --- |
| 2 | Batteries, spare, APC 650 UPS | APC 650 | -- | USGS | Stored in cabinet marked for USGS, Event G-052-S |
| 1 | Trimble Power Supply, AC to 18VDC (spare) | SDA5518 |  | UNAVCO | Stored in cabinet marked for USGS, Event G-052-S |
| 1 | Trimble 3-way power/download cable (LEMO / serial / coax power) |  |  | UNAVCO | Stored in cabinet marked for USGS, Event G-052-S |
| 1 | Serial Cable, DB9, Female to Male connectors |  | -- | UNAVCO | Stored in cabinet marked for USGS, Event G-052-S |
| 2 | Cable: BNC to BNC, Male (spare) | RG58C, 50 Ohm | -- | UNAVCO | Stored in cabinet marked for USGS, Event G-052-S |
| 1 | DC power cable, Trimble NetR8 (LEMO to red/black unterminated leads) |  | UNAVCO # 17077 | UNAVCO | Stored in cabinet marked for USGS, Event G-052-S |
| 1 | Trimble NetR8 spare receiver, pre-configured | NetR8 | UNAVCO # 28922; S/N 5025K68496 | UNAVCO | Stored in cabinet marked for USGS, Event G-052-S Backup for “Primary” receiver. |
| 1 | Radio Shack regulated DC power supply |  |  | USGS | 13.8 volt, 3 amp |
| 1 | Radio Shack regulated DC power supply |  |  | USGS | This was used inside the V-8 vault for UNAVCO G-296 GPS prototype system 2008-2010, should reside back in the USGS cabinet now. |
| 1 | Hex wrench for SCIS antenna radome screws |  |  | USGS | In plastic bag in USGS cabinet. |
| 1 | GPS Networking antenna splitter with power supply | ALDCBS1x8 |  | USGS | 8-way splitter, Type N connections |
| 1 | Heavy antenna cable, 15 meter, N-N connections |  |  | USGS | Spare cable for receiver to antenna connection |
| 1 | 10 meter thin antenna cable, N-N connections with N-TNC adapter |  |  | USGS |  |
| 1 | WR GPS antenna splitter | LDCBS1x4 |  | USGS | 4-way, type N connections |
| 1 | System info binder |  |  |  | Blue 3-ring binder |
| 1 | Hand-held GPS receiver | Garmin GPS48 |  |  | USGS (?), with manual |